# I. Uniform Circular Motion

Uniform circular motion means an object that is going around in a circle at a constant speed. The velocity is continually changing as the direction of motion is always changing.

## 1. Centripetal Acceleration

Note that: (i) the instantaneous velocity,, is always tangential. This is the direction that a stone in a sling will actually go when the sling is released.
(ii) the acceleration is always towards the centre

Acceleration going towards the centre is called centripetal acceleration, ac. There is no such thing as centrifugal acceleration – acceleration that pushes something to the outside of a circle. (Think about it a bit. When you are in a car that is turning to the left, you are not being pushed to the outside (the right). You want to keep on going straight (Newton’s First Law). The reason that you don’t go straight is that the car is moving to the left, the side of the car also pushes you to the left! – that is to the inside of the circle!

and are perpendicular. If this wasn’t so, you wouldn’t go in a circle. If suddenly became zero, then the object would just go in the direction of  (the red arrow). If got smaller slowly, you would spiral into the centre.

## 2. Formula

Any acceleration towards the centre is related to the velocity and radius:

Obviously this is a scalar equation – it doesn’t give direction as both  and are constantly changing (so is for that matter). We also cannot divide vectors (we may be able to square them).

Now for a circle, the distance around it is 2(r and the time for one revolution is T.
 (v = 2(r/T or 2(rf. This means that our formula for acceleration can be written as

## 3. Centripetal Force

Any force that pushes something towards the centre of a circle is called centripetal force, Fc. This is the force that keeps something in circular motion. Centripetal Force is a “pseudo-force” in that there is always some other real force that is pulling the object in. Think of it as a way of describing or classifying other forces. Possible centripetal forces include gravity, tension, friction, the normal force, electromagnetic force.

All centripetal forces are also equal to Fc = mac 	which gives

Example: (1) How fast can you swing a 600g mass around your head on a 1.1m long string that will break when FT = 40 lbs?
What is the frequency of rotation? How long does it take for 1 cycle?
(2) The moon completes one around the earth in 27.3 days. How far away is the moon? mE = 5.98E24 kg

Homework: Nelson: p 126 #5 – 10

Giancoli: p132 #1, 5, 7, 12
*NOT MUCH ABOUT  GRAVITY – IT WILL ALL BE DONE IN THE FIELDS UNIT

# II. Cars Going around curves

For problems involving cars going around a curve, we use centripetal force and another (real) force.

Fc = mv2/r

The car will “want” to continue moving in a straight line, so there must be a force that pulls it in a circular path.

There are typically two forces that can do this on cars.

( 1. Consider a flat, unbanked, curve.  The force of friction (static friction since nothing is slipping) between the tires and the road is the centripetal force keeping the car on the circular road.
(How does this work? Think of a rollerblader – to go into a left turn he pushes his feet to the right: outward. The force of friction with the road causes the road to push him to the left.)

In this case,  Ff ( mv2/r	Which way does the > < sign go? You can have an enormous force of friction and it won’t affect things, but if it is too small, then the car will slide.

The meaning of mv2/r is that this is the minimum force needed for a car to be going in a circle.

( 2. Consider a banked curve. This is very nicely worked out in the Nelson 12 textbook (section 3.2).

If we ignore friction, then the force that is keeping the car in a circular path is the component of the normal force (from the road (perpendicular to the surface remember))  that points towards the centre of the curve.

You can calculate what this component is.  (some function involving force of gravity and sin( or cos().

This component is then ( mv2/r.

Sample Problems:

( 1. A flat unbanked curve. Let’s make up a problem.

What are the variables? mass, co-efficient of friction, speed, radius of the curve. 
Which three shall be given? Which one shall we solve for? r.

Let’s pick some numbers: 
m = 9,000 kg (a transport truck?),	 ( = 1.5, 	v = 90 km/hr = 25 m/s,
 r = ? (I would guess a fairly wide curve – like 20 m).
I’ll write this as a word problem: What is the smallest radius of curvature that a 9000 kg truck can navigate at 90 km/hr if the coefficient of friction between the tyres and the road is 1.5?

Ff = ( FN 	and FN = Fg				This frictional force is the centripetal force
    = 1.5 (9000kg)(9.8 N/kg)				( 	Fc = mv2/r
    = 132,300 N						Ff  = mv2/r

(mg = mv2/r

solving for r:  r = v2/(g

Hmm… by doing it algebraically, we see that the mass cancels out. You wouldn’t notice this if you just started putting numbers in. Note that this problem does not consider the truck going so fast that it flips over. We are only considering sliding sideways off of the curve.

r = (25m/s)2 / (1.5)(9.8 m/s2)

= 42.5 m

( 2. A banked curve with no friction (i.e. with a sheet of ice on it – like a bobsled run – if it is curved it can still keep the vehicle on the track.

Let’s make up a problem.

What are the variables? mass, angle banked, speed, radius of the curve. 
Which three shall be given? Which one shall we solve for? (

Choose some numbers: m = 1000 kg, r = 15 m, v = 60 km/hr

Write a word problem with this: At what angle should a 30m diameter curve be banked for a 1000 kg car to be able to stay on the road at 60 km/hr assuming icy conditions?

In this case it works best if we use x and y in the horizontal and vertical directions (because Fc is horizontal to the centre of the curve).
*** x is in the direction of the net force (Fc)

We can see two important things:
Fc = FNx			and	FNy = Fg
 


Draw a force triangle for FN   (

With some simple geometry, we can prove that the angle at the bottom of the triangle is ( - the same as the ramp angle.

From trig. we see that 
FNx = FN sin(		and FNy = FN cos(	we won’t need these relationship unless we need to find FN

(also:   tan( = FNx / FNy
 
If we substitute in from above …  tan( = Fc / Fg			tan ( = (mv2 /r ) / mg

.: tan ( = v2 / rg		Note that we never had to calculate values for FN or FNx (FNy = Fg)

Notice that the mass cancels out here too!

With numbers: tan( = (16.7m/s)2/(9.8 N/kg)(15m)

( = 62.21 degrees.

In real life this angle would be less because friction also keeps the car on the road, and there would be speed reduction signs for such a tight curve.

Homework:

Giancoli p 132 # 8,9 (fairly simple)  p 132 #17,18 are complicated – they combine friction with a slope. We won’t be doing this in this course. AP physics students should do these two questions.

Students think that centripetal acceleration means that the speed is always increasing. 
Constant speed in a circle = no acceleration!

But acceleration implies that either speed or direction changes (or both).

Example:

“A car is going around a curve (r=30m) at a speed of 60kph. Will it slide off the road if (=1.1 ? 
(assume the mass is 1234 kg).

When you have a problem like this, you have too much information. What is the unknown that you are trying to find? Make one of the known numbers something that you don’t know, and solve for it, then compare the answer to the number in the question in a logical fashion.

e.g. How fast can the car go around a 30m curve with (=1.1?

…

by doing this algebraically first, you can see that the masses cancel out.

v = 64 km/ph

Answer to original question: YES. The maximum speed is 64 kph, and you’re only going 60kph.

Method 2:

Find the force of friction that the car has  Ff = (FN  … = 13316N
Find the centripetal force needed to keep the car I na circle at that speed and radius
Fc = mv2/r … = 11426N

Yes, there is enough friction to keep the car on the road.

# Text boxes

Fg

FN

FNy    (    FN

FNx

v ( r   This means that the outer parts of a hard drive are accessed faster. The outer partitions are fastest!